## Slide 1: Topology Optimization Approach
Flat surface boiling calibration experiments
Evaluate heat sink performance
ΔT
ΔT
h
Extract hflat(ΔT)
from flat surface boiling experiments
q’’
Boiling
boundary condition
h(ΔT) at Гboiling
Heat input at Гheater
Heat conduction in Ω
Heat transfer model for boiling heat sink
A boiling calibration experiment is used to extract the heat transfer function hflat(ΔT), which serves as the boiling boundary condition for the heat sink conduction problem

## Slide 2: Topology Optimization Formulation
Design problem for topology optimization
Topology optimization strategy
Boiling
boundary condition
h(ΔT)
(from boiling test)
Heat input
Heat conduction
Design space:
(voxel representation)
Topology optimization formulations
f: Target function
g: Governing physics
ρ: Physical density
T: Temperature
Heated area
Heat transfer model for boiling heat sink
Converted design problem
Boiling heat sink governing equations
discretization

## Slide 3: Topology Optimization Workflow
ΔT
Heat Transfer Analysis
Sensitivity Analysis
Intermediate Design
Iterations
0
1
-0.02
0.02
Initialization
Final Design
Topology Optimization Formulations
f: Target function
g: Governing physics
ρ: Physical density
T: Temperature
Optimization Target

## Slide 4
“Topology optimization is a mathematical method that optimizes the material distribution within a design space for a given objective function.” [1]
Mathematical method: The formulation of the problem needs to be clearly defined
Material distribution: The optimized design is given as a map of material distribution within a design space.
Objective function: the target of topology optimization is to minimize the defined objective function.
Introduction to Boiling Heat Sink Topology Optimizations
S. Ozguc, L. Pan, J. A. Weibel, IJHMT, 2021
How to use topology optimization to design boiling heat sink?

## Slide 5
Convert the Heat Transfer Model for Topology Optimizations
To optimize the design, evaluating performance variations in response to design changes (gradient) is necessary.
For this reason, we describe the heat sink design as material density distribution ρ in a domain Ω
The domain Ω is discretized into voxels, and the heat sink is described by designating the density of each voxel
For final heat sink design, the density ρ of each voxel must either 0 or 1
The density can’t change abruptly from 0 to 1: this results intermediate design
The converted heat transfer model should still be able evaluate the “performance” when the density gradually changes from 0 to 1
Heat sink design as surface geometry
Heat sink design as material distribution (voxel)
Gradually Evolve the material distribution to optimize the heat sink design

## Slide 6
Heated area
Design Space: A field of physical density
Discretization into voxel cubes
Converted Heat Transfer Model for Topology Optimizations
Given the heat input, the boiling boundary condition hflat(ΔT), and the material distribution of a heat sink, solve the temperature distribution.
Material Distribution: Physical density field within the computational Domain.
Material property: defined as a function of physical density.
The boiling heat sink boundary: cells where physical density changes drastically from 1 to 0.
Boundary condition: modeled as sources terms at the heat sink boundary.

## Slide 7
Discretized Heat Transfer Model for Topology Optimizations
The design space is discretized into small voxels
Conduction between neighboring voxels is calculated as:
Interpolation scheme: solid isotropic material with penalization (SIMP)
Penalization parameters (Pk) is set to ensure the design correctly converges to “black and white” design.
P
N
N
N
N
In discretized form (2D for demonstration):
*Each cube has a side length of Δx
kmin is needed to avoid singularity

## Slide 8
Discretized Heat Transfer Model for Topology Optimizations
Convective heat loss of boiling between voxel P and N is defined as wall heat flux and applied as the source to voxel P:
Energy balance equation for voxel P is defined as:
The energy balance equations for each voxel (the governing physics) can then be written as a system of non-linear state equations:
P
N
N
N
N
In discretized form (2D for demonstration):
*Each cube has a side length of Δx

## Slide 9
Topology Optimization Formulations
Topology Optimization Formulations
Target function
Governing physics
ρ: Physical density
T: Temperature
The 3-dimensional temperature and physical density distribution are described by the vector of design variable ρ and the vector of state variable T
The design variable and the state variable must satisfy the governing physics g(ρ,T) = 0
For a heat sink design described by density field ρ, the temperature state T can be solved from the governing physics
The target function f evaluates the performance of a given design ρ and state T
Topology optimization optimize the design ρ to minimize the target f
ρ: Physical density field vector, or design variable
T: Temperature field vector, or state variable
Governing Physics
3-D density and temperature field
Design and State Variable Vector
Thermal resistance
mass

## Slide 10
Topology Optimization Strategy:
Topology Optimization Formulations
Target function
Governing physics
ρ: Physical density
T: Temperature
It is hard to directly find the minimum of a multi-variable function f. Instead, the design is iteratively updated to minimize the target f.
Gradient based method are used to calculate the update step Δρ at each iteration.
Specifically, we use the method of moving asymptotes (MMA), which is an optimization algorithm for non-linear programming problems.
Whatever iterative algorithm is adopted, the gradient of target f to design ρ needs to be calculated.
However, we don’t directly calculate dT/dρ. Instead, we use adjoint method to implicitly calculate it.
Adjoint Method

## Slide 11
ΔTbase (K)
q’’ (W/cm2)
Design evolution
Predicted performance of optimized design
h (W/cm2K)
ΔT (K)
h (ΔT) applied to the problem
Discretization:
120 × 120 × 32 voxels
Heat input:
900 W
Heat Sink Material:
Copper (390 W/mK)
Iteration : 4
50
200
500
8 mm
30 mm
30 mm
20 mm
20 mm
Computational domain
Rendered view of optimized heat sink
Y. Huang and J. A. Weibel (Manuscript In Preparation)
10
Boiling Heat Sink Optimization Example